## Slide 1: Journal of Saudi Chemical Society King Saud University

## Slide 2: AH Alghamdicomplexes with different organic ligands adsorbed on the elec
***START OF PAGE 2*** 2 A.H. Alghamdicomplexes with different organic ligands adsorbed on the elec- trode surface. Over the years a large number of chelating agents of various classes were used for the determination of more than sixty elements in almost all groups of periodic sys- tem of elements (Zaitsev et al., 1999). Dimethylglyoxime (DMG), 8-hydroxyquinoline (Oxine), nioxime, catechol, cup- ferron, tropolone and solochrome violet RS are some selected examples of such very popular chelating agents. Alizarin is a natural dye and chelating agent, which has been used success- fully in the stripping voltammetric determination of some met- als including Mo (Tyszczuk and Korolczuk, 2008), Al(III) (Wang et al., 1987), In(III) (Zhao et al., 1996). The determination of trace concentration levels of zinc is of interest in different fields such as environmental surveillance, food control and occupational hazards (Venugopal and Luc- key, 1978; Underwoodm, 1977). Because of the industrial sig- nificant of zinc and as well as its environmental concern, a sensitive and yet simple analytical method for its trace determi- nation is required. Accordingly, adsorptive stripping voltam- metry has been effectively employed for the determination of zinc ions in various real samples after its prior complexation with some organic surface-active substances such as Morin (Shams et al., 2004), 2-quinolinethiol (Paneli and Voulgaropo- ulos, 1994, tetramethylene dithiocarbamate (TMDC) Hernan- dez-Brito et al., 1993, ammonium pyrrolidine dithiocarbamate (APDC) Ornella et al., 1995; Van, 1985, propyl gallate (Young et al., 2003), carbidopa (Gholivand et al., 2007) and xylenol or- ange (Colston and Robinson, 1997). The present work examines the reliability and validity of SW-AdSV electrochemical method for the determination of trace amounts of zinc in food samples via the application of alizarin as a chelating agent.2. Experimental 2.1. Apparatus All square-wave adsorptive stripping measurements were car- ried out with 797 AV computrace (Metrohn, Herisau, Switzer- land) in connection with Dell computer and controlled by (VA computrace 2.0) control software. Stripping voltammograms were obtained via a Hewlett–Packard laser jet printer. A con- ventional three electrode system was used in the hanging mer- cury drop electrode (HMDE) mode. This three electrode system was completed by means of a platinum auxiliary elec- trode and an Ag/AgCl (3 M KCl) reference electrode. Atomic absorption spectrometric determination of zinc metal was achieved by Perkin–Elmer Flame Atomizer (Model 2280). The pH was measured with Metrohn 744 pH meter. Oxford adjustable micropipette (Ireland) was used to pipette microliter volumes standard solutions. 2.2. Reagents All chemicals used were of analytical reagent grade and were used without further purification. Stock solution of Zn(II) of 1 · 10?2 mol?1 was prepared by dissolving the appropriate amount of nitrate salts (BDH, UK) in distilled water in 100- ml volumetric flasks. A 1 · 10?2 mol?1 stock solution of aliza- rin (BDH, UK) was prepared by dissolving an accurately weighed amount of pure substances. Standard solutions of zincmetal ions or ligands with lower concentration were prepared daily by diluting the stock solutions with distilled water. Britton–Robinson supporting buffer (pH ? 2, 0.04 mol l?1 in each constituent) was prepared by dissolving 2.47 g of boric acid (Winlab, UK) in 500 ml distilled water containing 2.3 ml of glacial acetic acid (BDH, UK) and then adding 2.7 ml of ortho-phosphoric acid (Riedal-deHaen, Germany) and dilut- ing to 1 l with distilled water. The carbonate buffer was 0.1 mol l?1 in both sodium hydrogen carbonate (Winlab, UK) and disodium carbonate (BDH, UK), while phosphate buffer was prepared from 0.1 mol l?1 in both phosphoric acid (Rie- dal-deHaen, Germany) and sodium dihydrogen phosphate (Winlab, UK). The acetate buffer was prepared from 0.02 M in both sodium acetate (Winlab, UK) and acetic acid (BDH, UK). Five different brands of popular instant coffee samples were purchased from city of Riyadh markets. 2.3. Procedure The general procedure adopted for obtaining square-wave adsorptive stripping voltammograms was as follows: a 20 ml aliquot of an appropriate buffer at desired pH was pipetted in a clean and dry voltammetric cell and the required standard solutions of the alizarin chelating agent and zinc metal ion were added. The test solutions were purged with nitrogen for 5 min initially, while the solution was stirred. The accumula- tion potential of ?0.1 V versus Ag/AgCl was applied to a new mercury drop while the solution was stirred for 60 s (un- less otherwise stated). Following the preconcentration period, the stripping was stopped and after 10 s had elapsed, cathodic scans were carried out over the range from 0.0 to ?1.3 V. For the analysed foodstuff samples (instant coffee) a pretreatment conventional wet digestion method utilizing acid mixture was applied. All measurements were obtained at room temperature.3. Results and discussion 3.1. Preliminary observations For test solution (acetate buffer pH 3) containing 5 · 10?6 mol l?1 Zn(II), preliminary stripping voltammetric measure- ments should that zinc ions exhibited a very weak and nearly flatted electrochemical peak at Ep = ?958 mV (versus Ag/ AgCl reference electrode) as can be seen from Fig. 1 (line A). However, the addition of 3 · 10?7 mol l?1 alizarin to the previ- ous acetate supporting electrolyte solution provided a well-de- fined (line B) cathodic peak at ?952 mV. In fact, the zinc ions exhibited a good affinity towards alizarin molecules forming a very stable alizarin–Zn(II) complex which is strongly adsorbed onto the HMDE surface. This obtained well-developed strip- ping voltammetric peak was found to response perfectly to the extra addition of either 5 · 10?7 mol l?1 alizarin or 5 · 10 7 mol l?1 Zn(II) (lines C and D, respectively), which probably reflect the formation and adsorption of the suggested complex. The observed SW-AdSV peak is most probably due to the cathodic reduction of Zn(II) in the adsorbed complex with alizarin and the electrochemical mechanism of the reduction process of alizarin–Zn(II) complex is illustrated in Fig. 2. Clearly, this proposed electrochemical reduction mecha- nism suggested an irreversible reductive process for zinc ions ***END OF PAGE 2***

## Slide 3: Figure Cyclic voltammogram for the formed complex between
***START OF PAGE 3*** Figure 3 Cyclic voltammogram for the formed complex between 1 · 10?7 mol l?1 Zn(II) and 5 · 10?7 mol l?1 alizarin in pH 3 acetate buffer at 50 mV s?1 scan rate. Figure 1 Square-wave adsorptive stripping voltammetric scan of Zn(II) in the presence of alizarin: A = acetate buffer pH 3 + 5 · 10?7 mol l?1 Zn(II), B = A + 3 · 10?7 mol l?1 alizarin, C = A + B + 5 · 10?7 mol l?1 alizarin and D= A+ B + C+ 5 · 10?7 mol l?1 Zn(II). Determination of zinc by square-wave adsorptive stripping voltammetry using alizarin as a chelating agent 3in the adsorbed complex, an assumption which was confirmed by cyclic voltammetric measurement of 1 · 10?7 mol l?1 Zn(II) ions and 5 · 10?7 mol l?1 alizarin chelating agent in pH 3 ace- tate buffer at 50 mV s?1 scan rate. As can be noticed from Fig. 3, which exhibits the cyclic voltammogram of alizarin– Zn(II) complex, the absence of the anodic peak at the reverse scan for the stripping voltammetric peak at ?831 mV con- firmed the irreversible nature of the evaluated reduction pro- cess. The first electrochemical peak observed at 655 mV in the given cyclic voltammogram is more probably resulted from the cathodic reduction of the electroactive anthraquinone moi- ety in the alizarin free molecules. Furthermore, when repetitive cyclic voltammetric measurements for alizarin complex with Zn(II) were carried out, a well-developed SW-AdSV peak was observed at ?841 mV for the first cathodic scan, however,O O OH +2 e- Figure 2 Mechanism of the electrochemical redsucceeding cathodic scans exhibit a gradual decrease in the vol- tammetric peak intensity, that seemed to indicate the adsorp- tive characteristic of this complex at the surface of the employed working electrode. Anyhow, the interfacial accumu- lation of this ligand–metal ion complex onto the HMDE sur- face can be used as an effective accumulation step in order to enhance the electroanalytical determination of zinc ions. 3.2. Optimum parameters and experimental conditions 3.2.1. Effect of pH The sensitivity of the SW-AdSV approach for the electrochem- ical analysis of Zn(II) metal ion via their formed complex with alizarin, is strongly dependent upon the pH and nature of sup- porting buffer which are the main factors influencing the for- mation of the observed complex, its stability, its adsorption process and its electrochemical reduction process. Among the investigated supporting electrolytes (acetate, phosphate, car- bonate and Britton–Robinson buffer) at different pH values, the best voltammetric peak resolution and sensitivity have been observed when utilizing 0.1 mol l?1 carbonate buffer, which will be selected for all subsequent experiments. The influence of pH value of the used buffer solution on the monitored stripping voltammetric peak current and potential was also investigated. When the SW-AdSV peak current of 5 · 10?7 mol l?1 Zn(II) in the presence of 1 · 10?6 mol l?1 aliz- arin was measured as a function of pH over the range 7.5–11.5, the zinc voltammetric signal was found to increase steadily over the examined pH range as can be seen from Fig. 4. How-O + Zno uction process for alizarin–Zn(II) complex. ***END OF PAGE 3***

## Slide 6: Figure Effect of pH on SWAdSV signal of mol l ZnII with mol l alizarin in acetate buffer after s
***START OF PAGE 4*** Figure 4 Effect of pH on SW-AdSV signal of 5 · 10?7 mol l?1 Zn(II) with 1 · 10?6 mol l?1 alizarin in acetate buffer after 90 s accumulation time at 0.0 V accumulation potential and 500 mV s?1 scan rate. 4 A.H. Alghamdiever, a sharp peak current decline was observed at pH 11.5, thus carbonate buffer solution with pH 11 seems to be the appropriate choice to ensure the highest voltammetric peak current. In addition, it was observed that the peak potentials for Zn/alizarin complex exhibited a shift in the negative direc- tion by 149 mV, when pH value was varied over the 7.5–11.5 pH range. 3.2.2. Effect of alizarin ligand concentration Varying the concentration of alizarin chelating agent also plays an important role in the investigated stripping voltam- metric procedure. Fig. 5 indicates that an increase of alizarin concentration from 1 · 10?7 to 1 · 10?6 mol l?1 at a constant Zn(II) concentration of 1 · 10?7 mol l?1 initiate a steady enhancement for the current intensity of the monitored SW- AdSV signal. However, addition of higher alizarin concentra- tion level (2 · 10?6 mol l?1 – 4 · 10?6 mol l?1) caused leveling off of the voltammetric peak height. Accordingly, it seems that alizarin concentration of 1 · 10?6 mol l?1 might be adequate to ensure maximum stripping voltammetric, hence, for further work this chelating agent concentration was selected.0.000000 0.000001 0 Alizarin C Figure 5 Effect of alizarin concentration on the stripping voltammet after 90 s accumulation time at 0.0 V accumulation potential and 5003.2.3. Effect of accumulation time and potential Fig. 6 illustrates the relationship of the stripping voltammetric peak current versus accumulation time for 1 · 10?7 mol l?1 Zn(II) with 1 · 10?6 mol l?1 alizarin over various adsorption times. Variation of the accumulation time over the range 0– 150 s at a preconcentration potential of 0.0 V showed a grad- ual enhancement for Zn(II) SW-AdSV peak current up to 60 s and decreased with longer preconcentration times. As a consequence, accumulation time of 60 s was selected as an optimum for further studies. When the adsorption of formed alizarin–Zn(II) complex was measured as a function of accumulation potential at 60 s collection time over the range from +0.2 V to ?0.8 V, it was observed that monitored peak current increased slightly when applying ?0.1 V as the optimal accumulation potential. 3.2.4. Effect of potential sweep conditions The scan rate parameter of the voltammetric technique was also varied in order to establish the optimum scan rate for the developed SW-AdSV procedure. It was found that the aliz-.000002 0.000003 0.000004 oncentration (M) ric peak current of 5 · 10?7 mol l?1 Zn(II) in pH 11 acetate buffer mV s?1 scan rate. ***END OF PAGE 4***

## Slide 7: Scan Rate mVs
***START OF PAGE 5*** Scan Rate (mV/s) Figure 7 Effect of scan rate on the stripping voltammetric peak height of 1 · 10?7 mol l?1 Zn(II) with 1 · 10?6 mol l?1 alizarin in pH 11 acetate buffer. Accumulation time: 60 s and accumulation potential: ?0.1 V. Accumulation Time (s) Figure 6 Effect of accumulation time on the SW-AdSV peak current of 1 · 10?7 mol l?1 Zn(II) with 1 · 10?6 mol l?1 alizarin in pH 11 acetate buffer. Accumulation potential: 0.0 V and scan rate: 500 mV s?1. Determination of zinc by square-wave adsorptive stripping voltammetry using alizarin as a chelating agent 5arin–Zn(II) SW-AdSV peak height increased gradually, over 100–1000 mV s?1 scan rate range. However, the width and the shape of the examined stripping voltammetric peak slightly distorted when utilizing scan rate higher than 700 mV s?1. Consequently, 700 mV s?1 scan rate is recommended as an optimal for subsequent electroanalytical studies. The depen- dence of SW-AdSV peak currents on scan rate is presented in Fig. 7. Moreover, the impact of varying the square-wave fre- quency on the SW-AdSV current intensity was also evalu- ated. The effect of this operating variable was studied over the range 20–90 Hz and it was concluded that in order to as- sure maximum peak current, 80 Hz square-wave frequency was the ideal choice for this operational parameter. Addition- ally, varying the value of excitation wave pulse amplitude also plays an important role for the measured stripping vol- tammetric current intensity. Increasing this parameter over the range 0.01–0.1 V, resulted in a substantial enhancement of the voltammetric peak current up to 0.06 V value and gradually decreased thereafter. Hence, for further electro- chemical investigation, 0.06 V excitation wave pulse ampli- tude value was adopted.3.2.5. Effect of instrumental parameters The monitored SW-AdSV peak current can be further maxi- mized by optimizing other experimental factors that can affect the adsorption accumulation process for the formed alizarin– Zn(II) complex. The influence of the surface size of the mer- cury drop working electrode on the observed stripping voltam- metric response was evaluated. The relationship between the measured peak current and the surface area of the drop was found to be linear for the surface areas of 0.15–0.60 mm2. For optimal sensitivity, 0.60 mm2 drop surface area (drop size 8) will be used for all next electrochemical measurements. In addition, the effect of convection rate was also studied by ascending the stirring rate from 100 to 3000 rpm. Although 3000 rpm stirring rate provided the maximum peak height, yet, 2000 rpm stirring speed was chosen as optimum value, which provided adequate preconcentration effect without affecting the drop stability. 3.3. Analytical performance Once the most ideal and suitable chemical conditions and instrumental parameters for the stripping voltammetric deter- ***END OF PAGE 5***

## Slide 8: Table Optimal conditions for voltammetric SWAdSV measurement of ZnII
***START OF PAGE 6*** Table 1 Optimal conditions for voltammetric SW-AdSV measurement of Zn(II). Parameter Studied range Optimal Supporting buffer Phosphate, B–R buffer, carbonate, acetate Carbonate buffer Alizarin concentration 1 · 10?7–4 · 10?6 mol l?1 1 · 10?6 mol l?1 Accumulation time 0–150 s 60 s Accumulation potential +0.3 V–(?0.8) V ?0.1 V Scan rate 100–1000 mV s?1 700 mV s?1 SW frequency 20–90 Hz 80 Hz Pulse amplitude 0.01–0.1 V 0.06 V Drop size 2–8 Size 8 Stirrer speed 100–3000 rpm 2000 rpm 6 A.H. Alghamdimination of zinc metal ions were established (Table 1), calibra- tion plot for this metal ion was recorded to estimate the ana- lytical characteristics of the developed SW-AdSV method. 3.3.1. Calibration graph and detection limit The dependence of alizarin–Zn(II) voltammetric peak current on the concentration of Zn(II) was obtained when successive additions of the standard Zn(II) solution were added to the voltammetric cell. As represented in Fig. 8, a proportional and linear relationship between Zn(II) and the monitored SW-AdSV signal was observed. Least squares analysis of the studied concentration range (5 · 10?8–4 · 10?7 mol l?1) yielded the following regression equation: ip ðnAÞ ¼ 911þ 5:94? 109 C ðmol L?1Þ r ¼ 0:996 n ¼ 5 where ip is the stripping voltammetric peak current in amperes, C is the analysed zinc metal ion concentration and r is the cor- relation coefficient. The effective preconcentration during the adsorption pro- cess of the formed complex makes it possible to achieve a very low detection limits. For this metal ion analysed via the opti- mized SW-AdSV procedure, the detection limit of 1 · 10?8 mol l?1 was calculated based on the signal-to-noise (S/ Zn(II) Conc Figure 8 Calibration graph for Zn(II) in the presence of 1 · 10?6 mol 0.1 V accumulation potential and 700 mV s?1 scan rate.3.3.2. Reproducibility and stability The high sensitivity of SW-AdSV approach is also accompa- nied by good precision of the obtained results. This can be attributed to the reproducible HMDE surface area and adsorption process for the formed alizarin–Zn(II) complex. Under the previously experimental optimized conditions, the reproducibility of the measured analytical signals was checked from 10 successive measurements of 1 · 10?7 mol l?1 Zn(II) in the presence of 1 · 10?6 mol l?1 alizarin. The precision of the method in terms of relative standard deviation was 1.3 RSD%. The stability of 1 · 10?7 mol l?1 Zn(II) solution was also investigated and monitored electrochemical signal was fond to give nearly a constant voltammetric current intensity up to 60 min. 3.3.3. Interference studies The major sources of interferences are likely to be from co- exciting metal ions capable of forming complexes with the used chelating agent, hence, affecting SW-AdSV response via an overlapping peak or competing for adsorptive sites or available ligand. The effect of the following ions, which are of great sig- nificance in industrial or environmental matrices, was tested at the optimal experimental conditions. As a matter of fact, the interfering metal ions were added at different concentrations2.50E-007 3.00E-007 3.50E-007 4.00E-007 4.50E-007 entration (M) l?1 alizarin in pH 11 acetate buffer after 60 s accumulation time at ***END OF PAGE 6***

## Slide 9: Table Practical application of SWAdSV for the determi
***START OF PAGE 7*** Table 2 Practical application of SW-AdSV for the determi- nation of zinc content in instant coffee samples and comparison with the results obtained by AAS technique. Instant coffee brand SW-AdSV (ppm) (ppm) Paired t-test value Nescafe Red Mug 1 507 ± 4 501 ± 30 t= 0.4 Nescafe Red Mug 2 707 ± 21 703 ± 40 t= 0.2 Nescafe Kanjara 719 ± 19 717 ± 43 t= 0.1 Bon café Classic 652 ± 3 663 ± 26 t= 0.7 Zidnee Classic 709 ± 34 714 ± 6 t= 0.2 Determination of zinc by square-wave adsorptive stripping voltammetry using alizarin as a chelating agent 7(1-fold, 5-fold and 20-fold) higher than the concentration of Zn(II) (1 · 10?7 mol l?1). Actually, very mild or no significant interference was observed upon adding 1-fold or 5-fold con- centration of Pb(II), Fe(III), Fe(II), Al(III) and Cd(II). How- ever, the presence of Cd(II) at higher concentration (20-fold) caused 19.8% decrease in zinc voltammetric peak current. On the other hand, the noticeable interference influence was observed when Cu(II) and Ni(II) metal ions were present in the test solution especially at higher concentration levels (20- fold). In fact, the monitored Zn(II) voltammetric peak height increased by 34% and 38% of its original height after the addi- tion of 20-fold of Cu(II) and Ni(II), respectively. Furthermore, the competitive effect of complexing agents on the Zn(II) SW-AdSV peak current was modeled by the additions of 5 · 10?7 mol l?1 and 1 · 10?6 mol l?1 of some other chelating agent such as EDTA, DMG and cupferone to the test solution. There was totally no effect for the addition of EDTA and DMG chelating agents at these concentration le- vel on the stripping voltammetric peak current of Zn(II) metal ion. However, a very mild increase in the SW-AdSV peak height by 5.7% after the addition of 1 · 10?6 mol l?1 cupfer- one ligand. 3.4. Analytical applications and accuracy In order to validate the practical reliability of the optimized SW-AdSV method, five different foodstuff samples (namely in- stant coffee) were analysed for their zinc contents by the rec- ommended voltammetric procedure (Table 1) after conventional wet digestion. In fact, zinc concentrations were calculated via the standard addition approach in order to min- imize the sample matrix interference. Typical analytical results correspond to the mean values of four replicate determinations are summarized in Table 2. The accuracy of the developed elec- troanalytical method was verified by comparing the analytical results obtained by SW-AdSV method with that obtained by atomic absorption spectrometric (AAS) method for the same instant coffee samples. As can be seen from Table 2, the results obtained by the developed voltammetric method compared favorably with those obtained by the spectroscopic reference method. The agreement of the compared result was tested by the paired t-test statistical approach (Miller and Miller,1994). The means of both analytical methods were found to be not differ significantly, since all the calculated t-test value were less than the critical value (2.45) at the 95% confidence level (P = 0.05). There is no statistical evidence that the means of the proposed voltammetric method differ significantly from the means of the reference methods (null hypotheses is obtained).Acknowledgements This work was supported by College of Science Research Cen- ter (Project No. ST/Chem/2007/35) and also was supported by King Abdulaziz City for Science and Technology (Project No. 15/28). The author would like to thank Mr. Monther Abdlka- reem for his technical assistance in applying the voltammetric method. References Abu Zuhri, A.Z., Wolfgang, V., 1998. Fresenius J. Anal. Chem. 360, Brainina, K.H., Neyman, E., 1993. Electroanalytical Stripping Meth- ods. John Wiley and Sons, New York. Brainina, K.H., Malakhova, N.A., Stojko, N.Y., 2000. Fresenius J. Colston, B.J., Robinson, V.J., 1997. Analyst 122, 1451–1455. Dewald, H.D., 1996. Stripping analysis. In: Winefordner, J.D. (Ed.), Modern Techniques in Electroanalysis. John Wiley and Sons, New York. Gholivand, M.B., Ahmadi, F., Sohrabi, A., 2007. Electroanalysis 19, Hernandez-Brito, J.J., Perez-Pena, J., Gelado-Caballero, M.D., Col- lado-Sanchez, C., 1993. Anal. Chem. Acta 284, 405–411. Miller, J.C., Miller, J.N., 1994. Statistics for Analytical Chemistry. Ellis Horwood, New York. Ornella, A., Maurizio, A., Giovanni, S., Corrado, S., Edoardo, M., Paneli, M.G., Voulgaropoulos, A.N., 1994. Fresenius J. Anal. Chem. Shams, E., Babaei, A., Soltaninezhad, M., 2004. Anal. Chem. Acta Tyszczuk, K., Korolczuk, M., 2008. Anal. Chem. Acta 624, 232–237. Underwoodm, E.J., 1977. Trace Elements in Human and Animal Nutrition. Academic Press, New York. Van der Berg, C.M.G., 1985. Marine Chem. 16, 121–130. B. Venugopal, T.D. Luckey, Metal Toxicity in Mammals, vol. 2, Chemical Toxicity of Metals and Metalliods, Plenum Press, New York, 1978. Wang, J., 1994. Analytical Electrochemistry. VCH Publisher Inc., New York. Wang, L., Chen, R., Wen, S., Zhu, J., 1987. Anal. Chem. 15, 118– Young, L.S., Woo, S.C., Hyun, K.L., Hoon, K.M., 2003. Georgia J. Zaitsev, P.M., Salikhdzhanova, R.M.F., Zaitsev, N.K., 1999. Indus. Zhao, J.Z., Sun, D.Z., Liu, D.J., 1996. Fenxi Huaxue 24, 101–103. ***END OF PAGE 7***